## Slide 1: An Open-Source Idea for Planning Integrated Circuit Layouts Efficiently :
IEEE TENCON 2024 (Singapore)
Nicholas Overacker a, b, Dr. James Stine a, Dr. Michal Ptaszynski b, Dr. Shingo Yoshizawa b, Miho Kobayashi c
a Oklahoma State University
b Kitami Institute of Technology
c Independent UI designer

## Slide 2: Background & Motivation

## Slide 3: Traditional LSI Design Stages[1]
1. Logic diagram
[1] J. D. Williams, “Sticks -- a new approach to lsi design,” Master’s thesis, Massachusetts Institute of Technology, June 1977.
2. CMOS circuit schematic
3. Topological diagram
4. Full Layout

## Slide 4: Topological “Stick” Diagrams
A freehand monochrome stick diagram from J.D. Williams’s 1977 thesis[1].
The same stick diagram redrawn with color-coding.
(¬C and f are relabeled as D and Y, respectively.)

## Slide 5: More about Stick Diagrams
Stick diagrams are used to:
  Visualize connections within an IC chip
  Plan final layout
  Estimate required die area
They are typically drawn freehand
  Fast and easy
  Length and width of lines don’t matter – only the relative positions of intersections!
But how can you validate a hand-drawn stick diagram?

## Slide 6: Validating Stick Diagrams
Stick diagrams can be complex
Visual inspection is error-prone
Fixing mistakes during final layout stage is difficult and time-consuming
Stixu is a CAD tool for the VLSI topological abstraction stage
A full adder stick diagram I drew & photographed in 2017.
[2] Ask me about this footnote during Q&A!

## Slide 7: Stixu Stick Diagrammer

## Slide 8: What is Stixu?
A browser-based tool for drawing and validating CMOS stick diagrams
For students, teachers, and researchers
Shows the whole output path of a circuit for any input
Source-available and free for non-commercial use
  https://github.com/NickOveracker/StickDiagrammer/
  There is not yet a safe and stable release that is suitable for business use
Try it on your phone: https://stixu.io/

## Slide 9: Getting Started
The best way to start is with the mobile interface
Simple and minimal UI
  … yet still full-featured!
Mobile-first design
The faster and more flexible PC UI is easy to learn after mastering the mobile interface.
Options and information
Dark mode
toggle
Active layer
indicator
Layer selector
Paint/Erase
toggle
Undo
Redo
I/O contact menu
Canvas
Add/Remove Columns
Add/Remove Rows
Shift entire grid
Generate & View Truth Table

## Slide 10: Output Analysis
Stixu produces 1 of 7 possible outputs for each input vector:
0 – Logical low (VSS / GND)
1 – Logical high (VDD )
Z – Floating (high impedance)
X – Indeterminate (short-circuit)
L – Unstable logic low (floating)
H – Unstable logic high (floating)
U – Unknown (no short-circuit)
Tap an output value to see the signal path!

## Slide 11: The Hypergraph Model
Stixu models stick diagrams as hypergraphs
  A generalization of traditional graphs
  Hyperedges can be connected to multiple vertices (i.e., nodes)
Vertices are individual primitive elements
  VDD, GND, inputs, outputs, transistor gate/source/node terminals, LO, and HI
Hyperedges are nets of primitive elements
Output values are found by testing paths from LO/HI to output vertices
  LO and HI are distinct from GND and VDD
    Not visible on the stick diagram

## Slide 12: Hypergraph Model Visualized
(A = 1, B = 1)
Notes: SYNCHRONIZE TIMING

## Slide 13: What does this contribute?

## Slide 14: What’s the Point?
Possibly the only free and publicly available stick diagramming tool
  Prior stick diagramming tools in the literature are ~40 years old and not publicly available
  A free and public tool contributes to the growing “open source silicon” movement
Useful in the classroom
  Students can easily experiment and gain intuition for stick diagrams
  Instructors can quickly validate diagram correctness
Useful for publications
  Authors can quickly illustrate, validate, and share circuit topologies
  Easier than using general drawing software such as MS Paint

## Slide 15: Tests and Limitations

## Slide 16: Testbench
All testbench cases can be seen at https://stixu.io/test
  51 different circuit topology test cases
    4 rotations * 2 reflections = 8 tests per topology
  8 UI interaction tests
    Dark mode toggle, add/remove terminals, etc
  1 “always fail” test
    Validates the testbench itself
Tested topologies range from a 5-stage inverter to a D flip-flop
Test 25: D latch

## Slide 17: Limitations
Floating gate analysis has O(2N) time complexity
  Scales with the number of floating gates (N)
  The problem reduces to the NP-Complete “BSAT” problem
  This is intrinsic to the task
  Perhaps heuristic approaches can be applied in constrained cases
Only static analysis
Purely digital – no consideration of analog effects
Difficult to rigorously validate the algorithm
  Currently only empirically validated
  Rigorous examination may be the topic of a future paper
Complex topologies with several floating gates take a significant amount of time to analyze. (Test 54, ~2s runtime)

## Slide 18: Next Steps

## Slide 19: Future Development Goals
Classroom integration features
  Homework assignment, submission, grading, etc.
Improved diagram saving/sharing/loading
  Currently only implemented by encoding circuit as a QR code
Modular design
  Use pre-made diagrams as black box modules for more complex, large-scale designs
Interoperability
  HDL generation, Magic layout generation
Area estimation, logical/electrical effort computation, and more!

## Slide 20: Thank you!
Nicholas Overacker
Kitami Institute of Technology (Master’s Year 2)
Oklahoma State University (B.S.)
nick.overacker@okstate.edu
m3235380013@std.kitami-it.ac.jp

## Slide 21: Themes
pdiff ndiff poly metal1 metal2 contact
Tol
Sorcery
Stix
Themes
Layers
Stixu has 3 palettes for layer colors
Tol is the default
  Colorblind-friendly
Sorcery is the Magic VLSI palette
Stix is the original Stixu palette